## Slide 1
Metal-Diamond Heat Spreader
Dynacard co. Ltd

## Slide 3
All Made in Taiwan
Welding — Opening a New Era of High-Power Chip Cooling
Reliable Mass Production
-- Fully In-House Technology Ensures Stable Supply to Global Server Leaders
Faster Delivery, Greater Reliability, Superior Cost Advantage
Twice as Fast-- Half the Delivery Time of Competitors
Delivering >600 W/m·K Superior Thermal Performance
Better Cost

## Slide 4
AI GPU power Consumption Roadmap

## Slide 5
High Heat Flux Packaging Design & Cooling Requirement
With TIM
With Solder(Liquid Metal) TIM
CHIP
TIM phaste, pad (3~20) W/(m·K)
Thermal Conductive Material
(Graphene or VC)
CHIP
Solder(liqiud Metal) 40~80 W/(m·K)
Thermal Conductive Material
(Cu-Diamond)
- Low vertical thermal conductivity
- Relies on TIM materials
- Up to 8× higher thermal resistance
- VC may dry out or leak
- Superior thermal conductivity
vertically and laterally.
- Direct soldering to the chip
- Extremely low interfacial thermal resistance
- Strong metal bonding

## Slide 6
Thermal Interface Development Stages
Minimal Thermal Resistance
& Max Efficiency
STAGE 03
CU-Diamond + Solder
+ Secondary Sintering
Secondary Sintering
High Interfacial
Thermal Resistance
STAGE 01
CU-Diamond + TIM1 + TIM2
TIM1 Resistance Reduced
STAGE 02
Cu-Diamond + Solder + TIM2

## Slide 7
Microchannel Heat Sink

## Slide 8
Effectively transfers heat to the coolant quickly
Spreads localized heat across the entire heatsink base
via the ultra-high thermal conductivity of diamond-copper,
ensuring rapid dissipation into the coolant
Designed for HPC
Heat dissipation requirements for
AI chips with power consumption of 1000W up

## Slide 9
Alleviating thermal stress and strain
Under specific conditions, diamond-copper's superior CTE
compatibility allows for a rigid attachment to the chip material.
Optimizing for lightweight design
Diamond-copper features a density just 60% of traditional copper.
Combined with optimized flow channels and hollow designs,
it delivers a weight savings of more than 30%, enabling a truly lightweight design.

## Slide 10
Grade | Thermal Conductivity @ 25 °C W/(m·K) | CTE 25 – 150 °C (ppm/°C) | Density (g/cm³) | Flexural Strength (MPa)
DC600 | 600 – 700 | 5.5 – 7.5 (Adjustable) | 5.2 – 5.4 | ≥ 280
DC700 | 700 – 800 | 5.5 – 7.5 (Adjustable) | 5.2 – 5.4 | ≥ 280
DC800 | 800 – 900 | 5.5 – 7.5 (Adjustable) | 5.2 – 5.4 | ≥ 280
DC900 | ≥ 900 | 5.5 – 7.5 (Adjustable) | 5.2 – 5.4 | ≥ 280
Grade | Thermal Conductivity @ 25 °C (W/m·K) | CTE 25 – 150 °C (ppm/°C) | Density (g/cm³) | Flexural Strength (MPa)
DA550 | 550 – 650 | 5 – 7 (Adjustable) | 3.1 – 3.3 | ≥ 350
DA650 | 550 – 650 | 5 – 7 (Adjustable) | 3.1 – 3.3 | ≥ 350
DA750 | ≥ 750 | 5 – 7 (Adjustable) | 3.1 – 3.3 | ≥ 350
Basic Physical Properties (Typical Values)
Cu-Diamond
(Copper matrix, diamond-reinforced)
Al-Diamond
(Aluminum matrix, diamond-reinforced)